## Slide 1
RENALIS
A dialysis twin that makes competing explanations and the next evidence question visible
RENALIS 0.4 1
Research prototype
Historical records + available device observations + explicit uncertainty
Notes: Project title and scope. Built-in patients are fictional. No clinical deployment or prospective benefit is claimed. Team and institution details must be supplied by the actual entrants before submission.

## Slide 2
The clinical research question
A declining pressure trace can fit several physiological explanations
RENALIS 0.4 2
During dialysis, fluid removal interacts with refill and compensatory responses.
RENALIS preserves several compatible models and compares hypothetical profiles.
The next question is which feasible observation could change that comparison.
Notes: Clinical motivation: KDIGO Blood pressure and volume management in dialysis, Kidney International 2020. https://kdigo.org/wp-content/uploads/2017/02/KDIGO-BP-Volume-Management-in-Dialysis-Conference-Report.pdf . Equations and noise values in RENALIS are authored research assumptions.

## Slide 3
One patient, one evidence cutoff
Six connected stages keep the reasoning visible
RENALIS 0.4 3
Learn from preceding sessions, then inspect the model state.
Compare four explanations, then preview possible measurement results.
Acquire or abstain, review the record, and inspect independent evaluations.
Notes: Live entry: /workspace?view=investigation&patient=RNL-014&minute=80 . Follow Learn, Understand, Compare, Ask, Review and Verify. The evidence journey is implemented in src/EvidenceJourney.tsx.

## Slide 4
Software architecture
The synthetic physiological path and observed-data benchmark remain separate
RENALIS 0.4 4
Preceding synthetic sessions
Raw BP + machine settings
History learner
Shrinkage + lineage digest
Current replay
Available-time cutoff
Four physiological families
48 particles per family
Observation-policy comparison
Time, noise, failure, burden
Evidence journey
Review + saved reports
Notes: Source: backend/history.py, model.py, mechanisms.py, app.py. React/TypeScript frontend, FastAPI/NumPy backend and SQLite persistence. Observed HEMOBP training is separate and does not drive synthetic physiological claims.

## Slide 5
Patient history changes the prior
Raw preceding-session trajectories replace an authored refill prior
RENALIS 0.4 5
Six completed synthetic sessions supply BP readings and machine settings.
A grid likelihood fits refill and compensation, then shrinks toward a population reference.
A forward-session ablation, uncertainty floor and history digest expose the learning limits.
Notes: Source: backend/history.py and history_fixtures.py. Current-session and future-available records are excluded. Generator and learner share a model family, so this synthetic ablation cannot establish clinical personalization.

## Slide 6
Inspectable physiological structure
Compartment state, measured settings and authored response maps are labeled separately
RENALIS 0.4 6
Tissue fluid
Estimated compartment
Circulating volume
Estimated compartment
Machine removal
Observed setting
Pressure response
Family-specific equation
Cardiac output
Authored sensor proxy
Vascular response
Authored hypothesis
Notes: Source: backend/model.py advance and backend/mechanisms.py project/sensor_prediction. Fluid conservation is tested. Conservation alone does not validate the pressure equation or identify a real physiological mechanism.

## Slide 7
Four explanations preserve ambiguity
Volume/refill, vascular, cardiac and mixed response families
RENALIS 0.4 7
Each family retains 48 particles and fits the same available BP and machine history.
Compatibility weights describe this chosen model bank and can remain unresolved.
Contradictory observations downgrade authority because actual physiology may be absent.
Notes: Source: backend/mechanisms.py. The mixed family expands authored possibilities but does not guarantee model completeness. Similar factual fits can imply divergent hypothetical responses. Family support is not a diagnostic probability.

## Slide 8
Possible measurements appear before acquisition
Predicted ranges include selected noise and observation timing
RENALIS 0.4 8
Cuff BP, relative blood volume and cardiac output have explicit observation equations.
Lower, middle and higher result previews show conditional support and scenario changes.
Overlapping ranges reveal when a measurement cannot reliably separate explanations.
Notes: Source: backend/insights.py. The UI shows conditional 10th to 90th ranges and three hypothetical outcomes. These previews are model-derived, uncalibrated and never enter the acquired-evidence ledger.

## Slide 9
Whole-policy observation value
The comparison includes what happens while waiting and when acquisition fails
RENALIS 0.4 9
Start with the best immediate action under the declared research loss.
Integrate possible results, delayed action and acquisition failure using Gaussian quadrature.
Subtract declared burden and delay penalty. Preserve negative value and abstain when needed.
Notes: Source: backend/mechanisms.py measurement_value. Nine-node Gaussian quadrature is compared with a 41-node diagnostic reference. Information gain remains distinct from expected decision-loss reduction. Costs and loss weights are authored, not elicited clinical utilities.

## Slide 10
An auditable evidence lifecycle
Availability, quality, corrections and saved revisions share one contract
RENALIS 0.4 10
Observe at minute t
Quality + declared noise
Release at minute t + delay
No future-value leakage
Assimilate valid evidence
Retain failures + artifacts
Append correction
Original value retained
Rewind before correction
Earlier evidence restored
Save immutable report
Revision + evidence IDs
Notes: Source: backend/app.py. Server enforces equipment, channel/value range and cutoff. Failed acquisitions remain charged and visible. Reset archives records. A correction appends a new value at its release time and preserves earlier cutoffs and saved reports.

## Slide 11
History adds a small retrospective gain
HEMOBP v3: 61,947 test windows from 176 separate test patients
RENALIS 0.4 11
Chart: mmHg
| Persistence | Dynamic | Demographics | Past sessions
MAE | 12.194 | 11.356 | 11.328 | 11.161
History increment: -0.1665 mmHg. Patient-cluster interval [-0.2298, -0.1099].
Notes: Source: docs/observed-v04.json and scripts/evaluate_observed_v04.py. Dataset DOI 10.6084/m9.figshare.6260654.v3, CC BY 4.0. https://www.nature.com/articles/s41597-019-0319-8 . Endpoint is next distinct measured SBP <=90 with a 5-35 minute gap and current SBP >90.

## Slide 12
The observed-data limits change interpretation
The clock-alignment assumption and alert workload remain visible
RENALIS 0.4 12
An empirical eight-hour table offset matches 2,516,989 of 4,366,298 machine packets.
Source clock semantics still need independent confirmation. Exclusions may bias the cohort.
Sensitivity is 61.25%, PPV is 13.51%, and empirical 90% range coverage is 86.74%.
Notes: Source: docs/observed-v04.json. Fit/calibration/test patient overlap is zero. Threshold selection uses calibration patients. Alerts consolidate under a 30-minute refractory rule. No continuous-event, prospective clinical or India transport claim follows from these figures.

## Slide 13
Decision value does not beat cuff overall
Independent authored holdout: 192 cases across eight regimes
RENALIS 0.4 13
Chart: Research loss units
| no observation | fixed cuff | information gain | decision value
Mean independent regret | 0.23078 | 0.2217 | 0.24472 | 0.24145
Decision value minus cuff: +0.01975, paired seed interval [-0.00981, 0.05996].
Notes: Source: docs/policy-validation-v04.json. All 768 policy records retained. Independent additive futures include mixed/omitted mechanisms, noise, basic equipment and delayed/failing acquisition. Oracle-grid metric amendment is documented and initial report preserved. No policies were tuned after evaluation.

## Slide 14
Failure states remain part of the product
A clear demonstration includes the cases where the model should stop
RENALIS 0.4 14
Current low BP, stale readings, completion and contradiction withhold scenario authority.
Failures and artifacts remain visible. Equipment constraints apply on the server.
Network errors disable mutations and offer retry. Reports preserve evidence through corrections.
Notes: Source: tests/test_model.py, tests/test_mechanisms.py, tests/test_research_release.py and scripts/check-journey.cjs. UI tests cover five responsive widths from 320 to 1440 pixels. Software tests do not establish clinical safety.

## Slide 15
Longitudinal and interoperability experiments
Both extensions expose their assumptions
RENALIS 0.4 15
Conditional fluid transport spans future sessions with authored intake/output and conservation checks.
A synthetic FHIR R4 collection exports Patient, Device and measured BP Observation resources.
Prospective physiology, ABDM profile conformance and authorized clinical integration remain open gates.
Notes: Source: backend/longitudinal.py and backend/app.py fhir_example. FHIR specification https://hl7.org/fhir/R4/observation.html and ABDM guide https://nrces.in/ndhm/fhir/r4/ . This is an example bundle, not a certification claim.

## Slide 16
The next evidence gates
A research prototype becomes credible through independent evidence
RENALIS 0.4 16
Confirm source clock semantics and reproduce the audited cohort independently.
Conduct an approved expert walkthrough and paired physiological silent study.
Evaluate external calibration and workload before any prospective impact or treatment claim.
Notes: Source: docs/clinical-study-protocol.md and docs/data-capture-schema.json. No recruited clinicians, approvals, measured staff-time savings or patient outcomes are claimed. Team identity and public submission links must be supplied and verified before entry.