## Slide 1
RENALIS
A dialysis twin that makes competing explanations and the next evidence question visible
RENALIS submission · 19 October 2026 1
Team Sigmoid
Rehaan · Solo entrant · JSS University, Noida
Competing explanations. A clearer next evidence question.
Notes: Project title and scope. Built-in patients are fictional. No clinical deployment or prospective benefit is claimed. Team Sigmoid, Rehaan (solo), JSS University, Noida; supplied by the entrant.

## Slide 2
The clinical research question
A declining pressure trace can fit several physiological explanations
RENALIS submission · 19 October 2026 2
During dialysis, fluid removal interacts with refill and compensatory responses.
RENALIS preserves several compatible models and compares hypothetical profiles.
The next question is which feasible observation could change that comparison.
Notes: Clinical motivation: KDIGO Blood pressure and volume management in dialysis, Kidney International 2020. https://kdigo.org/wp-content/uploads/2017/02/KDIGO-BP-Volume-Management-in-Dialysis-Conference-Report.pdf . Equations and noise values in RENALIS are authored research assumptions.

## Slide 3
One patient, one evidence cutoff
Six connected stages keep the reasoning visible
RENALIS submission · 19 October 2026 3
Learn from preceding sessions, then inspect the model state.
Compare four explanations, then preview possible measurement results.
Acquire or abstain, review the record, and inspect independent evaluations.
Notes: Live entry: /workspace?view=investigation&patient=RNL-014&minute=80 . Follow Learn, Understand, Compare, Ask, Review and Verify. The evidence journey is implemented in src/EvidenceJourney.tsx.

## Slide 4
Software architecture
The synthetic physiological path and observed-data benchmark remain separate
RENALIS submission · 19 October 2026 4
Preceding synthetic sessions
Raw BP + machine settings
History learner
Shrinkage + lineage digest
Current replay
Available-time cutoff
Four physiological families
48 particles per family
Observation-policy comparison
Time, noise, failure, burden
Evidence journey
Review + saved reports
Notes: Source: backend/history.py, model.py, mechanisms.py, app.py. React/TypeScript frontend, FastAPI/NumPy backend and SQLite persistence. Observed HEMOBP training is separate and does not drive synthetic physiological claims.

## Slide 5
Patient history changes the prior
Raw preceding-session trajectories replace an authored refill prior
RENALIS submission · 19 October 2026 5
Six completed synthetic sessions supply BP readings and machine settings.
A grid likelihood fits refill and compensation, then shrinks toward a population reference.
A forward-session ablation, uncertainty floor and history digest expose the learning limits.
Notes: Source: backend/history.py and history_fixtures.py. Current-session and future-available records are excluded. Generator and learner share a model family, so this synthetic ablation cannot establish clinical personalization.

## Slide 6
Inspectable physiological structure
Compartment state, measured settings and authored response maps are labeled separately
RENALIS submission · 19 October 2026 6
Tissue fluid
Estimated compartment
Circulating volume
Estimated compartment
Machine removal
Observed setting
Pressure response
Family-specific equation
Cardiac output
Authored sensor proxy
Vascular response
Authored hypothesis
Notes: Source: backend/model.py advance and backend/mechanisms.py project/sensor_prediction. Fluid conservation is tested. Conservation alone does not validate the pressure equation or identify a real physiological mechanism.

## Slide 7
Four explanations preserve ambiguity
Volume/refill, vascular, cardiac and mixed response families
RENALIS submission · 19 October 2026 7
Each family retains 48 particles and fits the same available BP and machine history.
Compatibility weights describe this chosen model bank and can remain unresolved.
Contradictory observations downgrade authority because actual physiology may be absent.
Notes: Source: backend/mechanisms.py. The mixed family expands authored possibilities but does not guarantee model completeness. Similar factual fits can imply divergent hypothetical responses. Family support is not a diagnostic probability.

## Slide 8
Possible measurements appear before acquisition
Predicted ranges include selected noise and observation timing
RENALIS submission · 19 October 2026 8
Cuff BP, relative blood volume and cardiac output have explicit observation equations.
Lower, middle and higher result previews show conditional support and scenario changes.
Overlapping ranges reveal when a measurement cannot reliably separate explanations.
Notes: Source: backend/insights.py. The UI shows conditional 10th to 90th ranges and three hypothetical outcomes. These previews are model-derived, uncalibrated and never enter the acquired-evidence ledger.

## Slide 9
After 3.74, the evidence question changes
The planner automatically focuses on the surviving volume–cardiac ambiguity
RENALIS submission · 19 October 2026 9
CO 3.74 L/min leaves cardiac 51.7% and volume 46.2% model support.
The next computed discriminator is relative blood volume, without a manual resolving value.
Actual synthetic RBV 85.0% shifts support to volume 66.9%, cardiac 31.8%: still unresolved.
Notes: Source: backend/discrimination.py, tests/test_discrimination.py and docs/demo-walkthrough-v04.md. Meera minute90, rate650, research equipment, noise1, failure0, immediate acquisition. Device fixtures are not accessible during selection. These are model-bank support weights, not clinical diagnostic probabilities.

## Slide 10
Why relative blood volume?
The two explanations predict different distributions, with honest overlap
RENALIS submission · 19 October 2026 10
Volume / refill
Median 83.87%
10th–90th:81.25–86.40%
Cardiac response
Median 87.81%
10th–90th:84.40–90.53%
Expected pair information: RBV 0.39378 bits; cuff 0.00004 bits.
Selected noise is included. The actual result may remain ambiguous.
Notes: Source: backend/discrimination.py 21-node Gaussian quadrature, current posterior, declared noise. Cardiac repeat at+5min offers0.00717 expected pair bits in this example. Pair metrics condition on these families, retaining other mass separately.

## Slide 11
Separate learning from improving a modeled action
The new information selector does not replace whole-policy decision value
RENALIS submission · 19 October 2026 11
Information ranks feasible observations by expected entropy reduction.
Decision value separately includes action loss, waiting, failure and burden.
The sequential selector is software-tested; independent multi-acquisition evaluation is still planned.
Notes: Source: backend/discrimination.py, backend/mechanisms.py and model-card.md. Two families with at least10% support trigger pair entropy; otherwise whole-bank entropy. Earliest feasible slot per channel;0.005-bit floor. Repeated observations assume independent noise. Frozen192-case study evaluated different one-acquisition policies.

## Slide 12
Whole-policy observation value
The comparison includes what happens while waiting and when acquisition fails
RENALIS submission · 19 October 2026 12
Start with the best immediate action under the declared research loss.
Integrate possible results, delayed action and acquisition failure using Gaussian quadrature.
Subtract declared burden and delay penalty. Preserve negative value and abstain when needed.
Notes: Source: backend/mechanisms.py measurement_value. Nine-node Gaussian quadrature is compared with a 41-node diagnostic reference. Information gain remains distinct from expected decision-loss reduction. Costs and loss weights are authored, not elicited clinical utilities.

## Slide 13
An auditable evidence lifecycle
Availability, quality, corrections and saved revisions share one contract
RENALIS submission · 19 October 2026 13
Observe at minute t
Quality + declared noise
Release at minute t + delay
No future-value leakage
Assimilate valid evidence
Retain failures + artifacts
Append correction
Original value retained
Rewind before correction
Earlier evidence restored
Save immutable report
Revision + evidence IDs
Notes: Source: backend/app.py. Server enforces equipment, channel/value range and cutoff. Failed acquisitions remain charged and visible. Reset archives records. A correction appends a new value at its release time and preserves earlier cutoffs and saved reports.

## Slide 14
History adds a small retrospective gain
HEMOBP v3: 61,947 test windows from 176 separate test patients
RENALIS submission · 19 October 2026 14
Chart: mmHg
| Persistence | Dynamic | Demographics | Past sessions
MAE | 12.194 | 11.356 | 11.328 | 11.161
History increment: -0.1665 mmHg. Patient-cluster interval [-0.2298, -0.1099].
Notes: Source: docs/observed-v04.json and scripts/evaluate_observed_v04.py. Dataset DOI 10.6084/m9.figshare.6260654.v3, CC BY 4.0. https://www.nature.com/articles/s41597-019-0319-8 . Endpoint is next distinct measured SBP <=90 with a 5-35 minute gap and current SBP >90.

## Slide 15
The observed-data limits change interpretation
The clock-alignment assumption and alert workload remain visible
RENALIS submission · 19 October 2026 15
An empirical eight-hour table offset matches 2,516,989 of 4,366,298 machine packets.
Source clock semantics still need independent confirmation. Exclusions may bias the cohort.
Sensitivity is 61.25%, PPV is 13.51%, and empirical 90% range coverage is 86.74%.
Notes: Source: docs/observed-v04.json. Fit/calibration/test patient overlap is zero. Threshold selection uses calibration patients. Alerts consolidate under a 30-minute refractory rule. No continuous-event, prospective clinical or India transport claim follows from these figures.

## Slide 16
Decision value does not beat cuff overall
Independent authored holdout: 192 cases across eight regimes
RENALIS submission · 19 October 2026 16
Chart: Research loss units
| no observation | fixed cuff | information gain | decision value
Mean independent regret | 0.23078 | 0.2217 | 0.24472 | 0.24145
Decision value minus cuff: +0.01975, paired seed interval [-0.00981, 0.05996].
Notes: Source: docs/policy-validation-v04.json. All 768 policy records retained. Independent additive futures include mixed/omitted mechanisms, noise, basic equipment and delayed/failing acquisition. Oracle-grid metric amendment is documented and initial report preserved. No policies were tuned after evaluation.

## Slide 17
Failure states remain part of the product
A clear demonstration includes the cases where the model should stop
RENALIS submission · 19 October 2026 17
Current low BP, stale readings, completion and contradiction withhold scenario authority.
Failures and artifacts remain visible. Equipment constraints apply on the server.
Network errors disable mutations and offer retry. Reports preserve evidence through corrections.
Notes: Source: tests/test_model.py, tests/test_mechanisms.py, tests/test_research_release.py and scripts/check-journey.cjs. UI tests cover five responsive widths from 320 to 1440 pixels. Software tests do not establish clinical safety.

## Slide 18
Longitudinal and interoperability experiments
Both extensions expose their assumptions
RENALIS submission · 19 October 2026 18
Conditional fluid transport spans future sessions with authored intake/output and conservation checks.
A synthetic FHIR R4 collection exports Patient, Device and measured BP Observation resources.
Prospective physiology, ABDM profile conformance and authorized clinical integration remain open gates.
Notes: Source: backend/longitudinal.py and backend/app.py fhir_example. FHIR specification https://hl7.org/fhir/R4/observation.html and ABDM guide https://nrces.in/ndhm/fhir/r4/ . This is an example bundle, not a certification claim.

## Slide 19
The next evidence gates
A research prototype becomes credible through independent evidence
RENALIS submission · 19 October 2026 19
Confirm source clock semantics and reproduce the audited cohort independently.
Conduct an approved expert walkthrough and paired physiological silent study.
Evaluate external calibration and workload before any prospective impact or treatment claim.
Notes: Source: docs/clinical-study-protocol.md and docs/data-capture-schema.json. No recruited clinicians, approvals, measured staff-time savings or patient outcomes are claimed. Team identity and public submission links must be supplied and verified before entry.