## Slide 1
RENALIS
Evidence-aware
dialysis digital twin
Competing explanations.
A better next measurement question.
TEAM SIGMOID
Rehaan / JSS University, Noida
Notes: Team details supplied by entrant. Research prototype. Conceptual generated cover illustration, not a real device or patient. Built-in patients/device streams are fictional. Artwork prompt and provenance: public/presentation-assets/provenance.json.

## Slide 2
One BP trace can support several explanations
An observation can narrow uncertainty without identifying a unique physiological cause.
RENALIS / Team Sigmoid / Research prototype
02
Chart: SBP (mmHg)
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90
Observed synthetic SBP | 148.5 | 146.3 | 144.5 | 142 | 141 | 134.8 | 133 | 128.4 | 129.6 | 127 | 125.8 | 116.2 | 113 | 110.5 | 111.3 | 103.7 | 103.7 | 96 | 95.9
Elapsed session minutes
The missing variable
Is the pressure change
more compatible with
volume, vascular or
cardiac response?
Synthetic replay at minute 90
Notes: Trace contains actual non-null available observations from film-data.json before cutoff90. No interpolation beyond the released data is shown. Clinical motivation: KDIGO BP and Volume Management in Dialysis Conference Report2020, https://kdigo.org/wp-content/uploads/2017/02/KDIGO-BP-Volume-Management-in-Dialysis-Conference-Report.pdf . Competing mechanisms remain authored research models.

## Slide 3
The research workspace
One evidence cutoff connects the patient replay, hypotheses and acquisition history.
RENALIS / Team Sigmoid / Research prototype
03
01
Learn
02
Understand
03
Compare
04
Ask
05
Review
06
Verify
Notes: Actual captured interface on an isolated synthetic database. Source: src/EvidenceJourney.tsx and video/submission_v05/capture.cjs. Patient RNL-014 at minute 90. Six journey sections are implemented, not a UI mockup.

## Slide 4
System containers
Current local implementation. Browser requests stay separate from offline evaluation.
RENALIS / Team Sigmoid / Research prototype
04
LOCAL RESEARCH WORKSPACE
User
Research review
Acquire + save
React workspace
TypeScript + Vite
Browser :5173
FastAPI service
Python + NumPy
HTTP JSON :8000
Twin + planner
History, state, hypotheses
Information + action loss
SQLite evidence store
Requests, readings, corrections
Saved experiment revisions
HTTP
JSON
Function calls
Transactions
Synthetic inputs
Authored BP/device replay
Six preceding sessions
Explicit acquisition fixtures
Published artifacts
Aggregate JSON, PDF/PPTX
Fictional FHIR collection
Versioned source + model card
Observed HEMOBP modeling runs offline and supplies evaluation reports, not the synthetic twin state.
Notes: Current implementation. Sources: backend/app.py PROJECT_DOCUMENTS, DB schema and endpoints; backend/model.py, history.py, mechanisms.py, discrimination.py, insights.py; src/api.ts; vite.config.ts. API functions run in one Python process, not separate microservices. SQLite is a local database. No NGINX, PostgreSQL, container orchestration, cloud deployment, authentication or live hospital integration is claimed.

## Slide 5
The prior comes from preceding sessions
Six completed synthetic sessions inform refill estimation before the current replay.
RENALIS / Team Sigmoid / Research prototype
05
Session trajectories
Raw BP + machine settings
Completed before current start
Likelihood fit
Refill / compensation grid
Uncertainty floor + shrinkage
Patient prior
Estimate + uncertainty
Source digest and fit lineage
What the interface exposes
Per-session fits, the fitted prior and the forward-session ablation make the learner inspectable.
6
preceding completed sessions
Notes: Source: backend/history.py and history_fixtures.py. History contains authored synthetic sessions. Shrinkage, source lineage and ablation expose assumptions; no clinical parameter identification is established.

## Slide 6
The physiological model
Estimated compartments connect removal, refill and family-specific pressure response.
RENALIS / Team Sigmoid / Research prototype
06
Tissue fluid
Estimated compartment
Circulating volume
Estimated compartment
Fluid removal
Observed machine setting
Refill
Removal
Pressure response
Volume sensitivity + compensation
Four authored response families
Current BP readings
constrain the hidden state.
A model state estimate
can remain ambiguous.
Notes: Source: backend/model.py advance/pressure and backend/mechanisms.py infer/project/sensor_prediction. The schematic is a computational compartment model, not an anatomical diagram or a clinically validated whole-body simulator.

## Slide 7
Four families fit the available past
Similar fit does not imply the same projected response.
RENALIS / Team Sigmoid / Research prototype
07
Volume / refill
24.9%
relative model support
1.87 mmHg
past-fit RMSE
Vascular response
25.0%
relative model support
1.86 mmHg
past-fit RMSE
Cardiac response
25.0%
relative model support
1.83 mmHg
past-fit RMSE
Mixed response
25.1%
relative model support
1.80 mmHg
past-fit RMSE
Notes: Values: film-data.json before, Meera/RNL-014 minute 90, hypothetical constant650mL/h. Each family has48 particles. Weights quantify relative compatibility inside this model bank, not diagnostic probabilities. Physiology outside the bank may be absent.

## Slide 8
Cardiac output narrows the disagreement
An acquired low-output result still fits both volume depletion and limited cardiac response.
RENALIS / Team Sigmoid / Research prototype
08
3.74
L/min acquired cardiac output
Cardiac 51.7%
Volume 46.2%
Current model support
Notes: Actual synthetic acquisition and posterior: film-data.json afterCO and interface capture. Source backend/measurement_fixtures.py. Output can fall with depleted circulation or limited modeled cardiac response. This reading does not identify a unique cause.

## Slide 9
How the acquired evidence changes support
The planner recomputes the full bank after each result. Residual ambiguity remains visible.
RENALIS / Team Sigmoid / Research prototype
09
Chart: Relative model support
| BP only | After CO 3.74 | After RBV 85.0
Volume / refill | 0.2493 | 0.4617 | 0.6693
Vascular response | 0.2499 | 0.0001 | 0
Cardiac response | 0.2502 | 0.5166 | 0.3178
Mixed response | 0.2505 | 0.0216 | 0.0128
Support is conditional on the authored model bank. It is not a probability of clinical diagnosis.
Notes: All four series and all three states are literal values from film-data.json. Percentages may have minor rounding error. New editable chart and embedded workbook snapshot preserve the source values. Cardiac51.66% / volume46.17% afterCO; volume66.93% / cardiac31.78% afterRBV.

## Slide 10
Why the next measurement is relative blood volume
The remaining families predict different noisy RBV distributions. Their ranges still overlap.
RENALIS / Team Sigmoid / Research prototype
10
Volume / refill
10th–90th: 81.25–86.40%
Median 83.87%
Cardiac response
10th–90th: 84.40–90.53%
Median 87.81%
80
82
84
86
88
90
92
% of starting blood volume
0.39378 bits
expected pair information
Notes: AfterCO snapshot adaptive planner. Volume median 83.87, 10th–90th81.25–86.40; cardiac87.81,84.40–90.53. Includes declared sensor SD 1.00% of start. Expected pair information0.39378 bits vs cuff0.00004 bits. Native range diagram represents displayed quantiles, not a fitted Gaussian curve. It does not promise resolution or treatment benefit.

## Slide 11
The device returns 85.0%
The acquired RBV shifts the balance toward volume / refill without eliminating cardiac support.
RENALIS / Team Sigmoid / Research prototype
11
66.9%
volume / refill support
31.8%
cardiac response support
Notes: Actual synthetic RBV85.0 result from film-data.json afterRBV. No manually chosen resolving5.4 is required. The newly recomputed planner may continue or stop depending on feasible expected separation and guards. This example remains ambiguous.

## Slide 12
Information and action value answer different questions
Both use current beliefs, but only one includes the modeled consequence of a decision.
RENALIS / Team Sigmoid / Research prototype
12
Information
Expected uncertainty reduction
Which feasible observation could
separate the remaining explanations?
Units: bits
Action value
Expected modeled loss reduction
Could the result improve the comparison
after waiting, failure and burden?
Units: declared research loss
Notes: Source: backend/discrimination.py and mechanisms.py measurement_value. Information bits and action loss are separate units and should not be subtracted from each other. A useful discriminator can have nonpositive net action value. Clinical utility has not been elicited or validated.

## Slide 13
Every observation has a lineage
Failures, artifacts and corrections remain distinguishable from evidence used in inference.
RENALIS / Team Sigmoid / Research prototype
13
01
Observe
Record physiological time and quality.
02
Release
Make evidence available after delay.
03
Correct
Append a reason and supersedes link.
04
Save
Keep revision and evidence in a snapshot.
Notes: Source: backend/app.py measurements, acquisitions and lab_runs schema; corrections endpoint. Observation and availability time have different meanings. Artifact values are retained but excluded from assimilation. Saved report revisions do not change after later corrections.

## Slide 14
History adds a small retrospective signal
HEMOBP v3. 61,947 test windows from 176 patients, with no patient overlap between splits.
RENALIS / Team Sigmoid / Research prototype
14
Chart: MAE (mmHg)
| Persistence | Dynamic | Demographics + dynamic | History + dynamic
Test MAE | 12.194 | 11.356 | 11.328 | 11.161
−0.1665
mmHg paired history increment
95% patient-cluster interval
[−0.2298, −0.1099]
Clinical importance
remains unestablished.
Notes: Source docs/observed-v04.json models and history_increment. History increment compares history+dynamic with demographics+dynamic on the same cohort. MAE12.194,11.356,11.328,11.161mmHg. Empirical clock shift and exclusions constrain interpretation. DOI10.6084/m9.figshare.6260654.v3; https://www.nature.com/articles/s41597-019-0319-8 .

## Slide 15
The evaluation still has material limits
A retrospective prediction result does not establish physiological identification or clinical benefit.
RENALIS / Team Sigmoid / Research prototype
15
61.25%
event sensitivity
13.51%
positive predictive value
86.74%
coverage of nominal 90% range
Clock alignment
The empirical 8-hour shift needs
independent confirmation.
Cohort exclusions
2,516,989 of 4,366,298 packets
match the declared checks.
Endpoint scope
Next measured BP differs from
continuous hypotension.
Notes: Source docs/observed-v04.json audit, interval and event_model. Endpoint requires currently non-low SBP and next distinct measured reading within5–35minutes. Missing events, false alerts and undercoverage remain visible. Raw observed data is not redistributed.

## Slide 16
Decision value does not beat cuff overall
Independent synthetic holdout: 192 cases, four policies and one acquisition per policy.
RENALIS / Team Sigmoid / Research prototype
16
Chart: Mean physiology regret
| No observation | Fixed cuff | Information gain | Decision value
Mean regret | 0.23078 | 0.2217 | 0.24472 | 0.24145
0.22170
fixed cuff
0.24145
decision value
Lower is better.
Notes: Source docs/policy-validation-v04.json. Mean regret0.23078no observation,0.22170fixed cuff,0.24472information gain,0.24145decision value. Earlier one-acquisition study. It does not validate current sequential selection. Paired decision-value delta vs cuff0.01975, interval[-0.00981,0.05996]. All768records and the metric amendment are retained.

## Slide 17
Authority changes with evidence quality
The service withholds scenario authority when the replay cannot support it.
RENALIS / Team Sigmoid / Research prototype
17
Current low BP
Current event is already present.
No advance-warning claim.
Stale or missing BP
Refresh the available evidence
before comparing scenarios.
Completed session
Do not compare new removal
profiles after session completion.
Contradictory evidence
Show poor fit and residual
uncertainty in the model bank.
Notes: Sources backend/app.py scenario guards, model.py alert states, mechanisms.py support_state, tests/test_model.py and test_discrimination.py. Current events, stale evidence and session completion block ranked scenario mutations. Poor model fit remains explicit. These are software guards, not a medical alarm specification.

## Slide 18
Extensions expose the next integration boundary
Current exports and transport experiments remain inspectable research components.
RENALIS / Team Sigmoid / Research prototype
18
Current compartments
Evidence-weighted volume state
Longitudinal transport
Authored intake / output
Mass-balance checks
Synthetic FHIR R4
Patient / Device / BP Observation
Reference + unit checks
FUTURE EXTERNAL INTEGRATION
Clinical systems
Live EHR access, governance
and ABDM conformance
require independent work.
Notes: Implemented backend/longitudinal.py, backend/fhir.py and app.py /longitudinal and /fhir. Compartment transport does not predict future BP or identify renal function. FHIR R4 collection is fictional and not certified for ABDM. Source standard https://hl7.org/fhir/R4/observation.html and https://nrces.in/ndhm/fhir/r4/ . Future integration is dashed and not an implemented connection.

## Slide 19
The next evidence gates
The strongest next work tests the assumptions that limit interpretation.
RENALIS / Team Sigmoid / Research prototype
19
01
Source timing
Confirm HEMOBP clocks
and reproduce the cohort.
02
Human interpretation
Test whether reviewers
understand ambiguity.
03
Matched physiology
Calibrate the model against
paired clinical measurements.
04
Independent policies
Predeclare multi-acquisition
budgets and correlated noise.
05
External silent study
Measure calibration and
workflow burden externally.
Notes: Proposed work, not completed studies. Sources: docs/clinical-study-protocol.md, data-capture-schema.json, implementation-decisions-v04.md and model-card.md. Clinical collaborators, approvals, enrollment and prospective impact are not claimed.

## Slide 20
A clearer next evidence question
RENALIS makes the model disagreement, the next observation and the remaining uncertainty visible.
RENALIS / Team Sigmoid / Research prototype
20
See the actual
20-minute demonstration
youtu.be/ZcWNYMtM1tI
github.com/RAK2315/RENALIS
Team Sigmoid
Rehaan
JSS University, Noida
Evidence and methods
Model card + source modules
Observed and policy reports
Research dossier + study protocol
Notes: Public source https://github.com/RAK2315/RENALIS and unlisted video https://youtu.be/ZcWNYMtM1tI . Sources and interpretations are in per-slide notes and README, docs/model-card.md, docs/observed-v04.json, docs/policy-validation-v04.json, research dossier and study protocol. No universal novelty or patient outcome benefit is claimed.